## Slide 1: MATLAB processing techniques for soil moisture and matric potential data
John Shuler
Boise State University
GEOS597
12/5/2016

## Slide 2: Soil is a main driver of precipitation routing
Notes: Precipitation falls on the landscape and is partitioned into various fluxes
Soil plays crucial role in nature of these fluxes

## Slide 3: Soil moisture and tension are common parameters of interest
Characteristic curves reveal soil properties
[Hillel, 1998]
Notes: Units of each
Usually derived in a lab setting; usually some hysteresis
Briefly define field capacity and wilting point

## Slide 4: Soil properties can be inferred from in situ time series data
[Chandler et al., 2016]

## Slide 5: DCEW Study Site and Instrumentation
Data Con 1 East Soil Profile:
5 moisture sensors (also measure temperature)
4 matric potential sensors
Measurements collected every 15 minutes from 5/12/16 to 9/30/2016
Notes: Briefly explain soil moisture sensors and matric potential sensors here
GET A FIELD SITE CLOSE TO THE ROAD

## Slide 6: Workflow Chart
Notes: Note bulk of work takes place during temperature correction

## Slide 7: Raw soil temperature data
Issues:
Data gap in early June

## Slide 8: Processed soil temperature time series
Notes: Good for long term trend, not for analyses where amplitude data is necessary

## Slide 9: Raw matric potential data
Issues
  Spikes and dropouts
  Data gap in early June
  Diurnal fluctuations

## Slide 10: Processed matric potential time series
Processing ignores diurnal fluctuations (for now)
Notes: Interpolated in similar manner to temp data but over shorter time span for Sensor 3

## Slide 11: Raw soil moisture data
Issues:
Data gap in early June
Diurnal fluctuations in shallow sensors
Notes: To assess if fluctuations are truly on a 24-hr period
First must select subset with relatively little trend

## Slide 12: Code for periodogram of data subset

## Slide 13: Is temperature-correction of VMC data justified by periodicity?

## Slide 14: Temperature correction a la Cobbs and Campbell, 2007
Method requires manual selection of 3 rain-free, 24-hour periods
Temperature correction equation uses multiple linear regression
Coefficients for MLR produced by the Matlab regress() function:

## Slide 15: Processed soil moisture data

## Slide 16: Incomplete Characteristic Curves

## Slide 17: To-Do List for Future John
Continue data collection to improve characteristic curves
Explore periodicity of matric potential data
  Use low-pass filter to correct for temperature?
Relate moisture and matric potential to stable isotope data

## Slide 18: References
Chandler, D., M. Seyfried, J. McNamara (2016), Inference of Soil Hydrologic Parameters from Electronic Soil Moisture Records. In review for Hydrologic Processes
Cobos, D. and C. Campbell, (2007) Correcting temperature sensitivity of ECH2O soil moisture sensors, Decagon Devices, Pullman, WA
Hillel, D. (1998) Environmental Soil Physics: Fundamentals, Applications, and Environmental Considerations, 1st Edition, Academic Press, Cambridge, MA
Lu, M., J. Kapilaratne and I. Kaihotsu (2015), A data-driven method to remove temperature effects in TDR-measured soil water content at a Mongolian site. Hydrological Research Letters, 9(1), 8–13 DOI: 10.3178/hrl.9.8